## Slide 1
BIOENERGY CRETE SA
Biogas / Electricity / Organic Fertilizers / Biomethane
Ioannis Petrakakis
Biogas Plant Manager
October 2021

## Slide 2
A “Green” Challenge for
Sychem Group
www.sychem.gr

## Slide 3: The 3D Challenge – The key for sustainable development
DECARBONISATION
Avoid CO2 or CH4 (GHG) emissions by using RES and energy integration techniques
DECENTRALISATION
To minimize the carbon footprint most of the water and energy systems must become local and decentralized
DIGITALISATION
Decentralized units and efficient integration need advanced control methods and can be only viable though digitalization

## Slide 4: Advantages of Biogas Plant
Green energy production from the biodegradation of organic waste
Solution to the organic waste management problem in a particularly environmentally- friendly way
Significant contribution to energy self-sufficiency of the country, replacing polluting or
imported fuels
Reduction of air, subsoil and water resources pollution due to the replacement of conventional power stations for energy production

## Slide 6: Raw Materials
Poultry and pig
manure
Oil-mills organic
residue
Whey
Slaughterhouse
waste
Expired food from super markets
Organic Waste (leftovers) from restaurants and hotels
Oils and Fats
Butcher shop
waste
Fish leftovers

## Slide 7: Indicative Raw Materials from Fish industry by-products

## Slide 8: Indicative Raw Materials from Meat industry and butcher shops by-products

## Slide 9: Facility Process Flow
Man
sl
man
N
DIGESTER
FLARE
Whey, Oil-mill residues, pig manure (liquid)
Slau wast ani
o
p
Bl
Food ag p
ure, organic
udge, pig
ure (solid) PASTEURIZATIO
ghterhouse e, aquatic
mals, animal Crusher
rigin by-
roducts
ood, Fats MIXING TANK
left-overs, Crusher/
ricultural
roducts Separator
BIOGAS CLEANING
BIOGAS
CHP
THERMAL ENERGY
INTERNAL
CONSUMPTION
DIGESTATE
STORAGE TANK
FAN SEPARATOR +
MFT + DECANTER
WWTP (MBBR-
MBR-UF-RO)
Solid fraction
FERTILIZER
Liquid fraction
ELECTRICITY
ELECTRICAL
GRID
18

## Slide 10: Products
Electricity
Heating (self consumption and local district heating)
Solid Residue (excellent compost)
Pure Water

## Slide 11: Organic Compost Liquid & Solid of high added value
Products

## Slide 12: Challenges - Innovations
Reception & management of incoming raw materials
Odor control
system - biofilter
WWTP (MBR –
MBBR – UF – RO)
liquid digestate management

## Slide 13: Challenges - Innovations
Reception & management of incoming raw materials
18

## Slide 14: Challenges - Innovations
Odor control system - biofilter

## Slide 15: Challenges - Innovations
WWTP (MBR –
MBBR – UF – RO)
liquid digestate management
Installation of wastewater treatment plant (MBR & BioBoost)

## Slide 16: Challenges - Innovations
WWTP (MBR –
MBBR – UF – RO)
liquid digestate management
Installation of wastewater treatment plant
(MBR & BioBoost)
Decanter

## Slide 17: Challenges - Innovations
WWTP (MBR –
MBBR – UF – RO)
liquid digestate management
Installation of Ultrafiltration membranes (UF)
Double system

## Slide 18: Challenges - Innovations
WWTP (MBR –
MBBR – UF – RO)
liquid digestate management
FINAL PRODUCT PURE WATER

## Slide 19
Statistics

## Slide 20: Raw Materials – type & quantity
48%
20%
17%
5%
10%
2020
16.947 tn
Poultry & pig manure
Expired food from S/M & food leftovers from hotels/ restaurants
Whey
Slaughterhouse waste & meat/fish industry by- products
Butcher shop waste
Oils and Fats
1%

## Slide 21: Companies Served – Circular Economy
80 companies & biowaste producers
18 organic compost clients

## Slide 22: Total CO2 emission Savings
65.529.863 km
252.238
9.273,44 tn
YEAR | SAVINGS |  | 
 | CO2 (tn/y) | TREES | CARS (km)
2017 | 1.033,32 | 28.106 | 7.301.876
2018 | 1.817,19 | 49.428 | 12.840.983
2019 | 2.213,09 | 60.196 | 15.638.578
2020 | 2.597,31 | 70.647 | 18.353.597

## Slide 23: Organic Compost

## Slide 24: Organic Compost – Drying Process

## Slide 25: Organic Liquid Soil Conditioner

## Slide 26
Biogas
to Biofuel

## Slide 27: Biogas to Biomethane
12/4/2022
SYCHEM GROUP OF COMPANIES

## Slide 28
“Production procedure”
Video

## Slide 29
12/4/2022
SYCHEM GROUP OF COMPANIES

## Slide 30
Awards and Distinctions

## Slide 31: 2019 - Two prestigious international awards for the innovative Biogas Plant in Crete - AD and Biogas Industry Awards, Birmingham, UK
“Most Circular City Award”
“Best Biogas Plant (on-farm, food waste or sewage) equal to or below 1 MWe- equivalent”

## Slide 32: International Publications in press for TECHNICAL BIOENERGY CRETE Project.
Bioenergy International, Digital Biogas Special 1, 2020

## Slide 33
BIOENERGY CRETE
www.bioenergycrete.gr info@bioenergycrete.gr